## Slide 1: Locking & Reservation Service
Andrew Nieuwsma
August 20, 2020

## Slide 2: Use cases
Protecting NCNs. We do need to be able to perform firmware updates and power control of NCNs but it's important that hardware management services cannot change the state of an NCN if another process is using the NCN.
Protect services from stepping on each-other. i.e. CAPMC may not power-off the device the FAS is updating.
Enable services to be able to coordinate with each-other via delegation; i.e. IFS calls BOS, BOS calls CAPMC, both IFS and CAPMC need lock control, so these services need a way to delegate lock control.

## Slide 3: Solution
Create an enhanced locking and reservation API that will allow us to manage hardware without jeopardizing the health and stability of the system.
Admins can take a lock -> does not expire, prevents any service from making a reservation
Services can take a reservation -> finite duration, can be renewed and delegated

## Slide 4: Gatekeepers
Services that have DIRECT hardware access (via Redfish and IPMI) are hardware gatekeepers. E.g. CAPMC, FAS, IFS, SCSD
If we can control the access to these services, then we can effectively control the management of the hardware.
Locking and reservations allows us to have a low level of coordination between services so that they do not interrupt each other.

## Slide 5: Charter
What we are trying to protect:
NCNs
Running compute jobs
Individual services from each-other
What we are preventing with a lock and reservation service:
Power state change
Firmware version change
Configuration change
What THIS is not:
Authz
Authn
Safety critical hardware controls
What we are NOT preventing with a lock and reservation service:
Registering for redfish alerting
Querying (GETs) via APIs to hardware
Discovery/Inventory

## Slide 6: How it works
The locking and reservation service must be integrated with the hardware gatekeeping services
This integration will ensure that these services HONOR the locks and reservations
Some services WILL have to change (at least a little bit)
We will deprecate this feature in State Manager, it will be its own service

## Slide 7: What we are making
API
  Lock
  Unlock
  Reserve
    Renew
    Release
    Delegate
  Break (EPO)
CLI – for admins
Client library (Go-lang)
Policy layer? TBD

## Slide 8: Thank you Questions?
Andrew.Nieuwsma@hpe.com